MeteoStation - Documentation

RX MODULE
Mikrokontroler:
Stellaris® LM4F120H5QR

Datasheet:
uC: http://www.mouser.com/ds/2/405/lm4f120h5qr-124014.pdf
devBoard: http://www.ti.com/tool/ek-lm4f120xl
Nice Pinout of the devboard : http://energia.nu/Guide_StellarisLaunchPad.html
PINOUT:
Device	Device pins	uC TI pins (PORT | PIN)
LCD SPFD5408	CS / RS / WR / RD / DATA LINES: / D15 / D14 / D13 / D12 / D11 / D10 / D9 / D8 / D7 / D6 / D5 / D4 / D3 / D2 / D1 / D0 / REST / LED_A	PD_6 / PE_1 / PE_2 / PE_3 / PC_7 / PC_6 / PC_5 / PC_4 / PD_3 / PD_2 / PD_1 / PD_0 / PB_7 / PE_0 / PB_5 / PB_4 / PB_3 / PB_2 / PB_1 / PB_0 / PF_4 / 3.3V
TOUCH CONTROLLER ADS7843, / RADIO RFM23 / SSI0	INT_IRQ / T_CS / T_CLK / T_DO / T_DIN / PIN_BUSY – not used / NSEL (CS) / NIRQ	PF_1 / PA_3 / PA_2 / PA_4 / PA_5 / PF_0 / PB_6 / #SSI0
ESP8266 / UART5	TXD0 / RXD0 / GPIO0 / GPIO2 / GPIO15 / EN / RST	PE_4 (RX) / PE_5 (TX) / 3.3V (GND for flashing) / 3.3V / GND / 10k resistor to 3.3V / 3.3V (GND to cause reset) / #UART5
USB micro		Already on the board
I2C	Future use	PA_6 (SCL) / PA_7 (SDA) / #I2C1
SD Card		NOT NEEDED ?